## Slide 1: Attention
答題內容請包含下列
  Please include the following content in your answer
  簡要操作流程（不必截圖，但須說明使用了那些工具）
    Brief operating procedure (no need for screenshots, but please explain which tools are used)
  答題可上網查詢包含引用ChatGPT，但必須註明引用來源，包涵ChatGPT
    You can use the internet and ChatGPT, but cite your sources and don't discuss with others.
  計算結果 Final Export
    出圖內容請包含圖例
      Please include a legend in the map
若題目要求進行 標準化（Normalization） 或 分級（Classification）：
  For tasks requiring Normalization or Classification:
  請採用 等距分級（Equal Interval） ，除非題目另有註明。
    Use the Equal Interval method unless otherwise stated.
  標準化值請設定介於 0–1 之間。
    Normalized values should range from 0 to 1.
所有結果請輸出成一個PDF
  Please upload all results as a PDF

## Slide 2: 花蓮地區多重災害風險分析 Multi-Risk Analysis in Hualien Area

## Slide 3: Data Sets:
花蓮地區的天然災害包含淹水、地震以及坡地災害，其中
  淹水災害影響因子包含
    1.淹水潛勢(Flooding_24h650)，風險判斷欄位:GRIDCODE
  地震災害影響因子包含
    2.土壤液化(Lique fration): ，風險判斷欄位:classify
    3.斷層帶（fault）:需自行環域100,300,500m分別代表 高,中,低
  坡地災害(Slope_Risk layer)影響因子包含
    4.土石流災害潛勢(debris): 風險判斷欄位:Risk 持續觀察:1,低:2,中:3高:4
    5.大規模崩塌(Large-scale Landslide):風險判斷欄位:Risk 低:1,中:2,高:3

## Slide 4: 花蓮縣村里人口資料 Population data of villages in Hualien County
COLUMN_NAME | DATA_TYPE | COLUMN_DESC | DISPLAY_UNIT
INFO_TIME | 文字 | 資料時間 | 
COUNTY_ID | 文字 | 縣市代碼 | 
COUNTY | 文字 | 縣市名稱 | 
TOWN_ID | 文字 | 鄉鎮市區代碼 | 
TOWN | 文字 | 鄉鎮市區名稱 | 
V_ID | 文字 | 村里代碼 | 
VILLAGE | 文字 | 村里名稱 | 
M_F_RAT | 數值 | 性比例(Male/Female) | 女=100
P_H_CNT | 數值 | 戶量(houses) | 人/戶
P_DEN | 數值 | 人口密度(density) | 人/平方公里 p/km2
DEPENDENCY_RAT | 數值 | 扶養比 Dependency | Ratio
A0A14_A15A65_RAT | 數值 | 扶幼比 Child dependency ratio | Ratio
A65UP_A15A64_RAT | 數值 | 扶老比 Elderly dependency ratio | Ratio
Total | 數值 | 總人口 | 人
Total_65 | 數值 | 老年總人口 | 人

## Slide 5: Question 1 Hazard Map
1.( 30%)：
  根據危險等級製作本地區全災害危害度等級分佈圖
    Plot all hazard map in this region according to the risk level
  Hint：
    將每種災害的風險等級值進行0~1的無因次化
    Normalize the risk levels of each type of disaster on a scale from 0 to 1
    如果屬性資料有null(空值) 可透過field calculator 以下兩種方法之一，計算式取代為0
      If the attribute data has null value, it can be replaced with 0 by the field calculator
      if("fieldname" is null, 0, "fieldname")
      coalesce( " fieldname" ,0)
    將該縣所有災害等級加總，再等分為三等級（低、中、高），分數介於0-1
      All hazard levels in the area are averaged and divided into Three equal levels (low, medium, and high), with scores ranging from 0 to 1

## Slide 6: Ans 1
將每個hazard 無因次化始值介於0-1之間
processtool -> union （multiple)
加總災害
  field calculator -> riskfld+…+ riskdebris
  去除null coalesce( " fieldname" ,0)
reclassify
  CASE
  WHEN "risk_all" <= minimum("risk_all") + (maximum("risk_all") - minimum("risk_all")) * 0.2 THEN 1
  WHEN "risk_all" <= minimum("risk_all") + (maximum("risk_all") - minimum("risk_all")) * 0.4 THEN 2
  WHEN "risk_all" <= minimum("risk_all") + (maximum("risk_all") - minimum("risk_all")) * 0.6 THEN 3
  WHEN "risk_all" <= minimum("risk_all") + (maximum("risk_all") - minimum("risk_all")) * 0.8 THEN 4
  ELSE 5
  END

## Slide 7: Question 2 Plot Risk analysis
2(30% )：
  請依照村里人口分佈之人口密度及扶老比等二項因子繪製五等級人口脆弱度圖
    Create a Five-Level Population Vulnerability Map Based on Population Density and Elderly Dependency Ratio
  Hint：
  由最低到最高進行等分標準化，分數介於0-1
    Normalize the scores evenly from the lowest to the highest, with scores ranging from 0 to 1.
  分別求各因子分數後再平均
    Calculate the scores for each factor separately, then take the average of the two to obtain the final vulnerability index.
3(20%)：
  請分別以人口密度及扶老比計算各村里五等級風險圖(危害度x脆弱度)
    Calculate Five-Level Risk Maps for Each Village Based on Population Density and Elderly Dependency Ratio (Hazard x Vulnerability)

## Slide 8: Ans 2-1
2-1
  Field calculator
    CASE
    WHEN "P_DEN" <= minimum("P_DEN") + (maximum("P_DEN") - minimum("P_DEN")) * 0.2 THEN 1
    WHEN "P_DEN" <= minimum("P_DEN") + (maximum("P_DEN") - minimum("P_DEN")) * 0.4 THEN 2
    WHEN "P_DEN" <= minimum("P_DEN") + (maximum("P_DEN") - minimum("P_DEN")) * 0.6 THEN 3
    WHEN "P_DEN" <= minimum("P_DEN") + (maximum("P_DEN") - minimum("P_DEN")) * 0.8 THEN 4
    ELSE 5
    END
CASE
WHEN "A65UP_A15A" <= minimum("A65UP_A15A") + (maximum("A65UP_A15A") - minimum("A65UP_A15A")) * 0.2 THEN 1
WHEN "A65UP_A15A" <= minimum("A65UP_A15A") + (maximum("A65UP_A15A") - minimum("A65UP_A15A")) * 0.4 THEN 2
WHEN "A65UP_A15A" <= minimum("A65UP_A15A") + (maximum("A65UP_A15A") - minimum("A65UP_A15A")) * 0.6 THEN 3
WHEN "A65UP_A15A" <= minimum("A65UP_A15A") + (maximum("A65UP_A15A") - minimum("A65UP_A15A")) * 0.8 THEN 4
ELSE 5
END
CASE
WHEN "Vul_avg" <= minimum("Vul_avg") + (maximum("Vul_avg") - minimum("Vul_avg")) * 0.2 THEN 1
WHEN "Vul_avg" <= minimum("Vul_avg") + (maximum("Vul_avg") - minimum("Vul_avg")) * 0.4 THEN 2
WHEN "Vul_avg" <= minimum("Vul_avg") + (maximum("Vul_avg") - minimum("Vul_avg")) * 0.6 THEN 3
WHEN "Vul_avg" <= minimum("Vul_avg") + (maximum("Vul_avg") - minimum("Vul_avg")) * 0.8 THEN 4
ELSE 5
END
  Vul_avg = ( "Vul_P_DEN" + "Vul_A65UP" )/2

## Slide 9: Ans 2-2
以下3種方法擇一
  Union
  Intersection
  Join attributes by location

## Slide 10: Question 3 預警性疏散
4(20% )：
  請評估馬太鞍溪堰塞湖預警疏散範圍內預計有多少人需要進行疏散？其中包含多少老年人口？
  Please estimate how many people are expected to be evacuated within the Matainan Creek landslide-dammed lake warning and evacuation area. How many of them are elderly?
  假設：人口平均分布在村里範圍內
  Assumption: The population is evenly distributed within the village boundaries.

## Slide 11: Ans 3
Intersection 撤離疏散範圍 ＋人口
Field calculator
  Area = $area /106 平方公里
  Pop = P_DEN * area
  pop * total_65/total

## Slide 12: 加分題：省道災害熱點與人口影響分析 Provincial Highway Disaster Hotspot and Population Impact Analysis
建立每條省道 500 公尺緩衝區（可依照省道編號）。
Create a 500-meter buffer for each provincial highway (based on the highway code if applicable).
統計各緩衝區內的災點數量，計算「每公里災點密度」。
Count the number of disaster points within each buffer and calculate the “number of disaster points per kilometer” (disaster density).
將災點密度最高的 2 條省道以紅色高亮顯示。
Highlight the three provincial highways with the highest disaster density in red.
疊合村里人口資料，估算位於第1高災害路段緩衝區內的總人口與老年人口。
Overlay the village population data and estimate the total population and elderly population located within the highest-risk highway buffer zones.

## Slide 13: Ans 加分題
Buffer 500m
Join attributes by location (summary)
  Count(fid)
Field calculator count / length(km)
Intersection 村里人口
Field calculator
  Area = $area /106 平方公里
  Pop = P_DEN * area
  pop * total_65/total

## Slide 14
請將訂正後結果於11/3前上傳至cool
期中考將以兩次分數平均計算